## Slide 1
ADC Programming
The ADC module in the LPC1768 uses the technique of successive approximation to convert signals from analog to digital values. The internal SAR (Successive Approximation Register) is designed to take the input from a voltage comparator of the internal module to give a 12-bit output resulting in a high precision result.
Va = ( Vref/212 )* Dval

## Slide 2
ADC Registers
Register | Description
ADCR | A/D COntrol Register: Used for Configuring the ADC
ADGDR | A/D Global Data Register: This register contains the ADC’s DONE bit and the result of the most recent A/D conversion
ADINTEN | A/D Interrupt Enable Register
ADDR0 - ADDR7 | A/D Channel Data Register: Contains the recent ADC value for respective channel
ADSTAT | A/D Status Register: Contains DONE & OVERRUN flag for all the ADC channels

## Slide 3
ADCR – A/D Control Register :
Bits[7:0] – SEL: Bit ‘x'(in this group) is used to select AD0.x
Bits[15:8] – CLKDIV: ADC Peripheral clock i.e. PCLK_ADC0 is divided by CLKDIV+1 to get the ADC clock.
Bit[16] – BURST: Set to 1 for doing repeated conversions, else 0 for software controlled conversions. Note: START bits must be set to 000 when BURST=1 or conversions will not start. The conversion is started scanning through the pins selected by bits set to ones in the SEL field. The first conversion corresponds to the least-significant 1 in the SEL field, then higher numbered 1-bits. Repeated conversions can be terminated by clearing this bit, but the conversion that’s in progress when this bit is cleared will be completed. If BURST is set to 1, the ADGINTEN bit in the ADINTEN register must be set to 0.

## Slide 4
Bit[21] – PDN : Set it to 1 for powering up the ADC and making it operational. Set it to 0 for bringing it in power down mode.
Bits[26:24] – START: These bits are used to control the start of ADC conversion when BURST (bit 16) is set to 0. 000 = No start, 001 = Start the conversion.
Bit[27] – EDGE: Set this bit to 1 to start the conversion on falling edge of the selected CAP/MAT signal and set this bit to 0 to start the conversion on rising edge of the selected signal. (Note: This bit is of used only in the case when the START contains a value between 010 to 111 as shown above.)
Other bits are reserved

## Slide 5
ADGDR – A/D Global Data Register : Contains the ADC’s flags and the result of the most recent A/D conversion.
Bits[15:4] – RESULT: When DONE bit = 1, these bits give a binary fraction which represents the voltage on the pin AD0.x. Value of 0x0 indicates that voltage on the given pin was less than, equal to or greater than VREFN. And a value of 0xFFF means that the input voltage was close to, equal to or greater than the VREFP.
Bits[26:24] – CHN: Represents the channel from which RESULT bits were converted. 000= channel 0, 001= channel 1 and so on.
Bit[30] – OVERRUN: In burst mode this bit is 1 in case of an Overrun i.e. the result of previous conversion being lost(overwritten). This bit will be cleared after reading ADGDR.
Bit[31] – DONE: When ADC conversion completes this bit is 1. When this register(ADGDR) is read and ADCR is written, this bit gets cleared i.e. set to 0. If ADCR is written while a conversion is in progress then this bit is set and a new conversion is started.
Other bits are reserved.

## Slide 6
ADDR0 to ADDR7 – A/D Data registers : This register contains the result of the most recent conversion completed on the corresponding channel [0 to 7]. Its structure is same as ADGDR except Bits[26:24] are not used/reserved.
Results of ADC conversion can be read in one of two ways.
One is to use the A/D Global Data Register to read all data from the ADC.
Another is to use the A/D Channel Data Registers.
It is important to use one method consistently because the DONE and OVERRUN flags can otherwise get out of synch between the ADGDR and the A/D Channel Data Registers, potentially causing erroneous interrupts or DMA activity.

## Slide 7
A/D Interrupt Enable register (ADINTEN )
This register allows control over which A/D channels generate an interrupt when a conversion is complete.
Bits[7:0] : Enable or disable the generation of interrupt upon the completion of a conversion on ADC channel [7:0]. Bit = 1 enables the interrupt and 0 disables
Bit 8: ADGINTEN: When set to 0, only the individual ADC channels enabled by ADINTEN7:0 will generate interrupts.
Remark: This bit must be set to 0 in burst mode
When set 1, only the global DONE flag in ADDR is enabled to generate an interrupt.
Other bits: Reserved

## Slide 8
ADSTAT – A/D Status register : This register contains DONE and OVERRUN flags for all of the A/D channels along with A/D interrupt flag.
Bits[7:0] – DONE[7 to 0]: Here xth bit mirrors DONEx status flag from the result register for A/D channel x.
Bits[15:8] – OVERRUN[7 to 0]: Even here the xth bit mirrors OVERRUNx status flag from the result register for A/D channel x
Bit 16 – ADINT: This bit represents the A/D interrupt flag. It is 1 when any of the individual A/D channel DONE flags is asserted and enabled to contribute to the A/D interrupt via the ADINTEN(given below) register.
Other bits are reserved.

## Slide 9
ADC modes in LPC1768:
Software controlled mode : In Software mode only one conversion will be done at a time. To perform another conversion we need to re-initiate the process. In software mode, only 1 bit in the SEL field of ADCR can be 1 i.e. only 1 Channel(i.e. Pin) can be selected for conversion at a time. Hence conversions can be done only any channel but one at a time.

## Slide 10
2. Burst or Hardware mode : In Burst or Hardware mode, conversions are performed continuously on the selected channels in round-robin fashion. Since the conversions cannot be controlled by software, Overrun may occur in this mode. Overrun is the case when a previous conversion result is replaced by new conversion result without previous result being read i.e. the conversion is lost. Usually an interrupt is used in Burst mode to get the latest conversion results. This interrupt is triggered when conversion in one of the selected channel ends.

## Slide 11
Setting up and configuring ADC Module for software controlled mode
Configure the appropriate PINSEL register for the desired function depending on the channel used.
To power up the ADC first the corresponding bit PCONP register must be set and then the PDN bit in ADCR must be set.
Also the bit corresponding to the channel and the START bit must be set
LPC_SC->PCONP |= (1<<12);
LPC_ADC->ADCR = (1<<4)|(1<<21)|(1<<24) // channel ADC0.4

## Slide 12
Fetching the conversion result in software controlled mode :
In software controlled mode we continuously monitor bit 31 in the corresponding channel data register ADDR. If bit 31 changes to 1 from 0, it means that current conversion has been completed and the result is ready. For example, if we are using channel 4 of AD0 then we monitor for changes in bit 31 as follows :
while(!(LPC_ADC->ADDR4 & 1<<31));
Then the result is extracted as follows:
adc_temp = (LPC_ADC->ADDR4>>4) & 0xFFF;

## Slide 13
Setting up and configuring ADC Module for Burst mode
In burst mode the START bit in ADCR is not used. In this case we can select multiple channels for conversion when setting up ADCR. The conversions start as soon the ADCR is setup.

## Slide 14
First the PINSEL register must be configured. Then configure the ADCR and ADINTEN as follows:
LPC_ADC->ADCR = (1 << 4 | 1 << 5 | 1 << 16 | 1 << 21); //AD0.4. AD0.5, Burst, PDN
LPC_ADC->ADINTEN = (1 << 4 | 1 << 5); //Enable int

## Slide 15
In Burst mode we use an ISR which triggers at the completion of a conversion in any one of the channel. Now, we just need to find the Channel for which the conversion was done. For this we fetch the channel number from ADGDR which also stores the conversion result. This can be read as follows:
int channel= (LPC_ADC->ADGDR>>24) & 0x7; //Extract Channel Number

## Slide 16
After knowing the Channel number, we have 2 options to fetch the conversion result from. Either we can fetch it from ADGDR or from ADDRx of the corresponding channel.
unsigned long t = LPC_ADC->ADGDR
int currentResult = (t>>4) & 0xFFF; //Extract Conversion Result
Ref:
http://www.ocfreaks.com/lpc1768-adc-programming-tutorial/

## Slide 17
Nested Vector Interrupt Control (NVIC)
In a microcontroller, interrupts serve as a way to immediately divert the central processing unit from its current task to another, more important task.
An interrupt can be triggered internally from the microcontroller (MCU) or externally, by a peripheral. The interrupt alerts the central processing unit (CPU) to an occurrence such as a time-based event a change of state, or the start or end of a process.

## Slide 18
Interrupts can be triggered internally – from a timer, for example – or externally, from peripherals.

## Slide 19
When an interrupt occurs, an interrupt signal is generated, which causes the CPU to stop its current operation, save its current state, and begin the processing program — referred to as an interrupt service routine (ISR) or interrupt handler — associated with the interrupt. When the interrupt processing is complete, the CPU restores its previous state and resumes where it left off.

## Slide 20
Nested vector interrupt control (NVIC) is a method of prioritizing interrupts, improving the MCU’s performance and reducing interrupt latency.
NVIC also provides implementation schemes for handling interrupts that occur when other interrupts are being executed or when the CPU is in the process of restoring its previous state and resuming its suspended process.
The term “nested” refers to the fact that in NVIC, a number of interrupts (up to several hundred in some processors) can be defined, and each interrupt is assigned a priority, with “0” being the highest priority. In addition, the most critical interrupt can be made non-maskable, meaning it cannot be disabled (masked).

## Slide 21
One function of NVIC is to ensure that higher priority interrupts are completed before lower-priority interrupts, even if the lower-priority interrupt is triggered first. For example, if a lower-priority interrupt is being registered or executed and a higher-priority interrupt occurs, the CPU will stop the lower-priority interrupt and process the higher-priority one first.

## Slide 22
The term “vector” in nested vector interrupt control refers to the way in which the CPU finds the program, or ISR, to be executed when an interrupt occurs. Nested vector interrupt control uses a vector table that contains the addresses of the ISRs for each interrupt. When an interrupt is triggered, the processor gets the address from the vector table.
The prioritization and handling schemes of nested vector interrupt control reduce the latency and overhead that interrupts typically introduce and ensure low power consumption, even with high interrupt loading on the controller.

## Slide 23
The Cortex-M3 processor uses a re-locatable vector table that contains the address of the function to be executed for a particular interrupt handler. On accepting an interrupt, the processor fetches the address from the vector table through the instruction bus interface. The vector table is located at address zero at reset, but can be relocated by programming a control register.
Ref:
https://www.motioncontroltips.com/what-is-nested-vector-interrupt-control-nvic/